SIMPLE MACHINES

LEVERS

- A lever is a simple machine that consists of a bar that pivots at a fixed point called a fulcrum.

First-Class Levers

- The fulcrum is between the input force and the load.

- Always change the direction of the input force.

Second-Class Levers

- The load of a second-class lever is between the fulcrum and the input force.

- Do not change the direction of the force, but allow for less force to be applied.

Third-Class Levers

- The input force is between the fulcrum and the load.

- Do not change the direction or amount of force.

PULLEYS

- A simple machine that consists of a wheel over which a rope, chain, or wire passes.

Types of Pulleys

- A fixed pulley is attached to something that does not move; changes the direction of the force.

- A movable pulley is attached to the object being moved; does not change the direction, but increases force.

- A block and tackle is when a fixed pulley and a movable pulley are used together.

WHEEL AND AXLE

- A simple machine consisting of two circular objects of different sizes; the wheel is larger of the two circular objects.

Mechanical Advantage of Wheel and Axle

- Can be found by dividing the radius of the wheel by the radius of the axle.

- MA is greater than 1 if the wheel is larger than the axle.

INCLINED PLANES

- A simple machine that is a straight, slanted surface, which facilitates the raising of loads.

- A ramp

Mechanical Advantage of Inclined Planes

- The greater the ratio of an inclined plane’s length to its height is, the greater the mechanical advantage.

WEDGES

- A simple machine that is made up of two inclined planes and the moves

- Often used for cutting.

Mechanical Advantage of Wedges

- The longer and thinner the wedge is, the greater its mechanical advantage.

SCREWS

- A simple machine that consists of an inclined plane wrapped around a cylinder.

- Screws are used most commonly as fasteners.

Mechanical Advantage of Screws

- The longer the spiral on a screw is and the closer together the threads are, the greater the screw’s mechanical advantage.

COMPOUND MACHINES

- A machine made of more than one simple machine.

Mechanical Efficiency of Compound Machines

- The mechanical efficiency of compound machines is low.

- Compound machines have more moving parts and therefore more friction to overcome.