## Slide 1: Work, Power and machines
Week of December 10th

## Slide 2: What is work?
Work is the transfer of energy to an object by using a force that causes the object to move in the direction of the force.
For work to be done on an object, the object must move in the same direction as the force.

## Slide 3: Work is done when…
1. the object moves as a force is applied.
2. the direction of the object’s motion is the same as the direction of the force.

## Slide 4: Calculating Work
W = F x d
Work is calculated by multiplying the force applied to the object by the distance through which the force is applied.

## Slide 5: Units
Force is expressed as Newtons (N)
Distance is expressed as meters (m)
Work is expressed as a newton-meter (N-m) or Joules (J)

## Slide 6: Joule
A joule is used to express energy.
A joule is equivalent to the amount of work done by a force of 1N acting through a distance of 1m in the direction of the force.

## Slide 7: Work Video Clip
http://www.learn360.com/ShowVideo.aspx?ID=639400

## Slide 8: Power
Power is the rate of which work is done or energy is transformed.

## Slide 9: Calculating Power
P = (W/t)
Power is work divided by time.
Power is expressed as a watt (W), which is equal to J/s

## Slide 10: Increasing Power
Power measures how fast work happens or how quickly energy is transferred.
Power increases when the time it takes to do a certain amount of work is decreased.

## Slide 11: Machines

## Slide 12: Journal Entry 12-12-12
Why do we use machines?

## Slide 13: What is a Machine?
A machine is a device that helps do work by either overcoming a force or changing the direction of the applied force.

## Slide 14: Work and Machines
Work input is the work you do on a machine.
Work output is the work done by a machine
The output force is the force the machine applies through a distance.

## Slide 15: How Machines Help
Machines change the size or direction of the input force.
Work output is never greater than work input, but the output force is applied over a greater distance.
Decreases the amount of force needed to do the same amount of work

## Slide 16: Mechanical Advantage
Mechanical advantage is a number that tells how many times a machine multiplies force.
It compares the input force with the output force.

## Slide 17: Calculating Mechanical Advantage
Mechanical advantage is equal to output force divided by the input force.

## Slide 18: Actual vs. Ideal Mechanical Advantage
Ideal Mechanical Advantage is calculated to represent the MA of the machine without friction.
Actual Mechanical Advantage is calculated to represent the MA of the machine with friction.

## Slide 19: Mechanical Efficiency
Mechanical Efficiency is a quantity usually expressed as a percentage, that measures the ratio of work output to work input.

## Slide 20: Mechanical Efficiency cont.
The less work a machine has to do to overcome friction, the more efficient the machine is.

## Slide 21: Ideal Machine
An ideal machine would be a machine that had 100% mechanical efficiency.

## Slide 22: Simple Machine Video
http://www.learn360.com/ShowVideo.aspx?ID=132365